## Slide 1
uGEMM: Unary Computing Architecture
for GEMM Applications
Di Wu, Jingjie Li, Ruokai Yin, Hsuan Hsiao (University of Toronto), Younghyun Kim and Joshua San Miguel

## Slide 2
Executive Summary
Review the demand of energy-efficient GEMM implementations, and motivate uGEMM over other unary approaches.
Demonstrate uGEMM’s compatibility for arbitrarily encoded inputs for multiplication and addition mathematically.
Prove the knob of uGEMM’s high energy efficiency to be early termination enabled by high accuracy and stability.
Notes: Provide more high level take aways.
Emph GEMM.
Goal of uGEMM: energy effieccnt, high acc, high stab, early term, compatible.

## Slide 3
Outline
Background
Motivation
Architecture
Evaluation

## Slide 4
GEneral Matrix Multiply (GEMM)
Ubiquitous in applications
  Computer vision
  Signal processing
  Machine learning
“At the center of Deep Learning”
  95% of GPU runtime
  89% of CPU runtime
Energy efficiency
  Unary computing as salvation
Y. Jia, “Learning Semantic Image Representations at a Large Scale,” PhD thesis.
Notes: Remove animation about binary

## Slide 5
Computing paradigm
Paradigm |  | Data | Bit significance | Computing domain
Binary computing | Bit parallel | Parallel | Varying | Spatial
 | Bit serial |  |  | 
Unary computing |  |  |  | 
b
co
s
a
ci
FA
b
co
s
a
ci
FA
b
co
s
a
ci
FA
b
co
s
a
ci
FA
0
Notes: Remove animation about binary

## Slide 6
Computing paradigm
Paradigm |  | Data | Bit significance | Computing domain
Binary computing | Bit parallel | Parallel | Varying | Spatial
 | Bit serial | Serial | Varying | Temporal
Unary computing |  |  |  | 
b
co
s
a
ci
FA
DFF

## Slide 7
Computing paradigm
Paradigm |  | Data | Bit significance | Computing domain
Binary computing | Bit parallel | Parallel | Varying | Spatial
 | Bit serial | Serial | Varying | Temporal
Unary computing |  | Serial | Equal | Temporal
0100 1000 0010 0010
1101 0110 1010 1011
1100 1010 1010 0010
16 bits
Unary Add
Notes: Black box add, non scale is good
Highlighting the data encoding method: weighted or not
Remove commers, using space

## Slide 8
Unary computing scheme
Scheme | Bit stream | Application
Stochastic computing | Rate coding | LDPC, image processing, machine learning
Race logic |  | 
1101 1000 1010 1010
8 1s
Bit stream as data.
Probability of 1s matters only.
SRC
RNG
CMP
…1010
…3819
…8888
Randomly determined
Notes: Randomly determined with a prob
Make bit-level animation more comphrehensive

## Slide 9
Unary computing scheme
0000 0000 1111 1111
8 1s
Bit stream as data.
Delay of 1s matters only.
SRC
CNT
CMP
…1111
…3210
…8888
Scheme | Bit stream | Application
Stochastic computing | Rate coding | LDPC, image processing, machine learning
Race logic | Temporal coding | DNA sequencing, decision tree, sorting
Deterministically determined
Notes: deterministicly determined with a prob
state that no coding will be mentioned till eval

## Slide 10
Unary computing data – bit stream
Unipolar value=0.5
Polarity | Binary width | Unary length | Probability of 1s | Value | Range
Unipolar | N | 2^N | P(1) | P(1) | Unsigned, [0, 1]
Bipolar |  |  |  |  | 
1101 1000 1010 1010
8 1s
Notes: Make bit-level animation more comphrehensive

## Slide 11
Unary computing data – bit stream
Bipolar value=0.0
Polarity | Binary width | Unary length | Probability of 1s | Value | Range
Unipolar | N | 2^N | P(1) | P(1) | Unsigned, [0, 1]
Bipolar |  |  |  | 2*P(1)-1 | Signed, [-1, 1]
8 1s
1101 1000 1010 1010
Notes: State unipolar is always used in following slides

## Slide 12
Measure of bit streams
Metric | Bit stream | Goal
Correlation | Two | How similar two bit streams are.
Stability |  | 
1101 1000 1010 1010
1101 1000 1010 1010
+1 correlation: count of aligned 1s is maximized.
Aligned 1 count: 8
8 1s
8 1s
Expected in temporal coding
Notes: +1 correlation first
More animations for aligned 1s.
And a 0 correlation, indepenance
-1 last
Use two bit streams
Remove the table snapshot?
Range and which is prefered

## Slide 13
Measure of bit streams
Metric | Bit stream | Goal
Correlation | Two | How similar two bit streams are.
Stability |  | 
0 correlation: count of aligned 1s is balanced.
1101 1000 1010 1010
1110 0100 0101 1010
Aligned 1 count: 4
8 1s
8 1s
1101 1000 1010 1010
1101 1000 1010 1010
+1 correlation: count of aligned 1s is maximized.
Aligned 1 count: 8
8 1s
8 1s
Expected in rate coding
Notes: +1 correlation first
More animations for aligned 1s.
And a 0 correlation, indepenance
-1 last
Use two bit streams
Remove the table snapshot?
Range and which is prefered

## Slide 14
Measure of bit streams
Metric | Bit stream | Goal
Correlation | Two | How similar two bit streams are.
Stability |  | 
1101 1000 1010 1010
1101 1000 1010 1010
+1 correlation: count of aligned 1s is maximized.
-1 correlation: count of aligned 1s is minimized.
0 correlation: count of aligned 1s is balanced.
1101 1000 1010 1010
1110 0100 0101 1010
1101 1000 1010 1010
0010 0111 0101 0101
Aligned 1 count: 8
Aligned 1 count: 4
Aligned 1 count: 0
8 1s
8 1s
8 1s
8 1s
8 1s
8 1s
Notes: +1 correlation first
More animations for aligned 1s.
And a 0 correlation, indepenance
-1 last
Use two bit streams
Remove the table snapshot?
Range and which is prefered

## Slide 15
Measure of bit streams
Metric | Bit stream | Goal
Correlation | Two | How similar two bit streams are.
Stability | One | How fast a bit stream converges to its desired value.
1101 1000 1010 1010
Stable point:
Error never exceeds a given threshold from now on.
Stability:
Ratio of stable cycle count to all.
Stability = 1-(7-1)/16 = 0.625
Chart: Cycle
 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
 | 0.5 | 0.5 | 0.16667 | 0.25 | 0.3 | 0.16667 | 0.071429 | 0 | 0.055556 | 0 | 0.045455 | 0 | 0.038462 | 0 | 0.033333 | 0
 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
 | 0.5 | 0.5 | 0.16667 | 0.25 | 0.3 | 0.16667 | 0.071429 | 0 | 0.055556 | 0 | 0.045455 | 0 | 0.038462 | 0 | 0.033333 | 0
Cycle 7
8 1s

## Slide 16
Measure of bit streams
Metric | Bit stream | Goal
Correlation | Two | How similar two bit streams are.
Stability | One | How fast a bit stream converges to its desired value.
1101 1000 1010 1010
Stable point:
Error never exceeds a given threshold from now on.
Stability:
Ratio of stable cycle count to all.
Stability = 1-(7-1)/16 = 0.625
1010 1010 1010 1010
Chart: Cycle
 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
 | 0.5 | 0.5 | 0.16667 | 0.25 | 0.3 | 0.16667 | 0.071429 | 0 | 0.055556 | 0 | 0.045455 | 0 | 0.038462 | 0 | 0.033333 | 0
 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
 | 0.5 | 0.5 | 0.16667 | 0.25 | 0.3 | 0.16667 | 0.071429 | 0 | 0.055556 | 0 | 0.045455 | 0 | 0.038462 | 0 | 0.033333 | 0
Chart: Cycle
 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
 | 0.5 | 0 | 0.16667 | 0 | 0.1 | 0 | 0.071429 | 0 | 0.055556 | 0 | 0.045455 | 0 | 0.038462 | 0 | 0.033333 | 0
Cycle 7
Cycle 4
Stability = 1-(4-1)/16 = 0.8125
8 1s
8 1s

## Slide 17
Measure of bit streams
Metric | Bit stream | Goal
Correlation | Two | How similar two bit streams are.
Stability | One | How fast a bit stream converges to its desired value.
1101 1000 1010 1010
Stable point:
Error never exceeds a given threshold from now on.
Stability:
Ratio of stable cycle count to all.
1010 1010 1010 1010
Chart: Cycle
 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
 | 0.5 | 0.5 | 0.16667 | 0.25 | 0.3 | 0.16667 | 0.071429 | 0 | 0.055556 | 0 | 0.045455 | 0 | 0.038462 | 0 | 0.033333 | 0
 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
 | 0.5 | 0.5 | 0.16667 | 0.25 | 0.3 | 0.16667 | 0.071429 | 0 | 0.055556 | 0 | 0.045455 | 0 | 0.038462 | 0 | 0.033333 | 0
Chart: Cycle
 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
 | 0.5 | 0 | 0.16667 | 0 | 0.1 | 0 | 0.071429 | 0 | 0.055556 | 0 | 0.045455 | 0 | 0.038462 | 0 | 0.033333 | 0
Cycle 7
Cycle 4
High stability enables early termination.
8 1s
8 1s
Stability = 1-(7-1)/16 = 0.625
Stability = 1-(4-1)/16 = 0.8125

## Slide 18
Outline
Background
Motivation
Architecture
Evaluation

## Slide 19
Unified uGEMM
Unified unary General Matrix Multiplication
  First to support Add/Mul in temporal coding
Notes: Compatibility for rate and temporal coding: support for all kinds of adders; add/mul insensitive to encoding.
Early termination: streaming, high acc, high stab

## Slide 20
Unified uGEMM
Unified unary General Matrix Multiplication
  First to support Add/Mul in temporal coding
  Compatibility for varying coding and polarity
Notes: Compatibility for rate and temporal coding: support for all kinds of adders; add/mul insensitive to encoding.
Early termination: streaming, high acc, high stab

## Slide 21
Unified uGEMM
Unified unary General Matrix Multiplication
  First to support Add/Mul in temporal coding
  Compatibility for varying coding and polarity
  Early termination
    Fully streaming computation

## Slide 22
Unified uGEMM
Unified unary General Matrix Multiplication
  First to support Add/Mul in temporal coding
  Compatibility for varying coding and polarity
  Early termination
    Fully streaming computation
    High accuracy and stability by solving the correlation problem

## Slide 23
Outline
Background
Motivation
Architecture
Evaluation

## Slide 24
Multiplication
  uMUL
    Unipolar and Bipolar
Addition
  Scaled (uSADD)
    Unipolar and Bipolar
  Non-Scaled (uNSADD)
    Unipolar and Bipolar (first support)
uGEMM overview
Notes: Overview of those units that leads to ugemm arch\
Mul ahead of add
Move example ahead of this intro.

## Slide 25
uGEMM – Multiplication
uMUL: unipolar
  Expected function

## Slide 26
uGEMM – Multiplication
uMUL: unipolar
  Expected function
  Actual AND gate function

## Slide 27
uGEMM – Multiplication
uMUL: unipolar
  Expected function
  Actual AND gate function
6/16
8/16=0.5
3/16
Correct with 0 correlation:
Marginal prob = conditional prob
3/6 = 0.5
Notes: Do you really need the equation to explain this? Just AND gate circuit should be enough.

## Slide 28
uGEMM – Multiplication
uMUL: unipolar
  Expected function
  Actual AND gate function
6/16
8/16=0.5
3/16
Wrong with non-0 correlation:
Marginal prob != conditional prob
6/6 = 1.0
Correct with 0 correlation:
Marginal prob = conditional prob

## Slide 29
uGEMM – Multiplication
uMUL: unipolar
  Conditional bit stream generation
    Enforce P(Sin, 1=1) = P(Sin, 1=1| Sin, 0=1)
C: Counter
G: Bit stream generator
en
SRC
RNG
CMP
Notes: Make a new slide for the counter and bit stream generator on right. Highlight takeaway from prev slide in bullet points maybe?

## Slide 30
uGEMM – Multiplication
uMUL: unipolar
2
1
2/4: 1 0 0 1
2/4
0 0 0 1
Sin,1 is static in counter.
2/4*2/4=1/4
Cycle | Counter (C) | RNG (G) | AND 0 (In 0) | AND 1 | Output
1 | 2 | 1 | 1 | 1 | 1
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
>

## Slide 31
uGEMM – Multiplication
uMUL: unipolar
2
3
2/4: 1 0 0 1
2/4
Sin,1 is static in counter.
0 0 0 1
2/4*2/4=1/4
Cycle | Counter (C) | RNG (G) | AND 0 (In 0) | AND 1 | Output
1 | 2 | 1 | 1 | 1 | 1
2 | 2 | 3 | 0 | 0 | 0
3 |  |  |  |  | 
4 |  |  |  |  | 
<
en

## Slide 32
uGEMM – Multiplication
uMUL: unipolar
2
3
2/4: 1 0 0 1
2/4
Sin,1 is static in counter.
0 0 0 1
2/4*2/4=1/4
Cycle | Counter (C) | RNG (G) | AND 0 (In 0) | AND 1 | Output
1 | 2 | 1 | 1 | 1 | 1
2 | 2 | 3 | 0 | 0 | 0
3 | 2 | 3 | 0 | 0 | 0
4 |  |  |  |  | 
<

## Slide 33
uGEMM – Multiplication
uMUL: unipolar
2
3
2/4: 1 0 0 1
2/4
Sin,1 is static in counter.
0 0 0 1
2/4*2/4=1/4
Cycle | Counter (C) | RNG (G) | AND 0 (In 0) | AND 1 | Output
1 | 2 | 1 | 1 | 1 | 1
2 | 2 | 3 | 0 | 0 | 0
3 | 2 | 3 | 0 | 0 | 0
4 | 2 | 3 | 1 | 0 | 0
<

## Slide 34
uGEMM – Multiplication
uMUL: unipolar
Cycle | Counter (C) | RNG (G) | AND 0 (In 0) | AND 1 | Output
1 | 2 | 1 | 1 | 1 | 1
2 | 2 | 3 | 0 | 0 | 0
3 | 2 | 3 | 0 | 0 | 0
4 | 2 | 3 | 1 | 0 | 0
1/4
2/4: 1 0 0 1
2/4
Sin,1 is static in counter.
0 0 0 1
2/4*2/4=1/4

## Slide 35
uSADD: unipolar
uGEMM – Scaled addition
Cycle | Input count (PC) | Accumulator (A) | Carry (output)
1 | 4 | 0 | 1
2 |  |  | 
3 |  |  | 
4 |  |  | 
0
4
3/4: 0 1 1 1
2/4: 0 1 0 1
1/4: 0 0 0 1
2/4: 1 0 0 1
(3/4+2/4+1/4+2/4)/4=2/4
1 0 0 1
Notes: Move the equations to the right of this slides

## Slide 36
uSADD: unipolar
uGEMM – Scaled addition
Cycle | Input count (PC) | Accumulator (A) | Carry (output)
1 | 4 | 0 | 1
2 | 1 | 1 | 0
3 |  |  | 
4 |  |  | 
1
1
3/4: 0 1 1 1
2/4: 0 1 0 1
1/4: 0 0 0 1
2/4: 1 0 0 1
1 0 0 1
+
(3/4+2/4+1/4+2/4)/4=2/4

## Slide 37
uSADD: unipolar
uGEMM – Scaled addition
Cycle | Input count (PC) | Accumulator (A) | Carry (output)
1 | 4 | 0 | 1
2 | 1 | 1 | 0
3 | 2 | 3 | 0
4 |  |  | 
3
2
3/4: 0 1 1 1
2/4: 0 1 0 1
1/4: 0 0 0 1
2/4: 1 0 0 1
1 0 0 1
+
(3/4+2/4+1/4+2/4)/4=2/4

## Slide 38
uSADD: unipolar
uGEMM – Scaled addition
Cycle | Input count (PC) | Accumulator (A) | Carry (output)
1 | 4 | 0 | 1
2 | 1 | 1 | 0
3 | 2 | 3 | 0
4 | 1 | 0 | 1
0
1
3/4: 0 1 1 1
2/4: 0 1 0 1
1/4: 0 0 0 1
2/4: 1 0 0 1
1 0 0 1
+
(3/4+2/4+1/4+2/4)/4=2/4

## Slide 39
uSADD: unipolar
uGEMM – Scaled addition
Cycle | Input count (PC) | Accumulator (A) | Carry (output)
1 | 4 | 0 | 1
2 | 1 | 1 | 0
3 | 2 | 3 | 0
4 | 1 | 0 | 1
2/4
3/4: 0 1 1 1
2/4: 0 1 0 1
1/4: 0 0 0 1
2/4: 1 0 0 1
1 0 0 1
(3/4+2/4+1/4+2/4)/4=2/4

## Slide 40
uSADD
  Expected function
  Carry overflow mechanism
    Parallel counter (PC) records current input.
    When accumulation (A) overflows, output logic 1.
uGEMM – Scaled addition
Notes: Overview of those units that leads to ugemm arch\
Mul ahead of add
Move example ahead of this intro.

## Slide 41
uNSADD: unipolar
Cycle | Input count (PC) | Acc (1) | Acc (3) | Acc (1>3) | Output
1 | 4 | 4 | 0 | True | 1
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
uGEMM – Non-scaled addition
4
4
0
0
1 1 1 1
3/4: 0 1 1 1
2/4: 0 1 0 1
1/4: 0 0 0 1
2/4: 1 0 0 1
Clip(3/4+2/4+1/4+2/4)=1
Anticipated
Historical
Notes: Remove offset in table and diagram

## Slide 42
uNSADD: unipolar
Cycle | Input count (PC) | Acc (1) | Acc (3) | Acc (1>3) | Output
1 | 4 | 4 | 0 | True | 1
2 | 1 | 5 | 1 | True | 1
3 |  |  |  |  | 
4 |  |  |  |  | 
uGEMM – Non-scaled addition
5
1
0
1
Clip(3/4+2/4+1/4+2/4)=1
3/4: 0 1 1 1
2/4: 0 1 0 1
1/4: 0 0 0 1
2/4: 1 0 0 1
1 1 1 1
+

## Slide 43
uNSADD: unipolar
Cycle | Input count (PC) | Acc (1) | Acc (3) | Acc (1>3) | Output
1 | 4 | 4 | 0 | True | 1
2 | 1 | 5 | 1 | True | 1
3 | 2 | 7 | 2 | True | 1
4 |  |  |  |  | 
uGEMM – Non-scaled addition
7
2
0
2
Clip(3/4+2/4+1/4+2/4)=1
3/4: 0 1 1 1
2/4: 0 1 0 1
1/4: 0 0 0 1
2/4: 1 0 0 1
1 1 1 1
+

## Slide 44
uNSADD: unipolar
Cycle | Input count (PC) | Acc (1) | Acc (3) | Acc (1>3) | Output
1 | 4 | 4 | 0 | True | 1
2 | 1 | 5 | 1 | True | 1
3 | 2 | 7 | 2 | True | 1
4 | 1 | 8 | 3 | True | 1
uGEMM – Non-scaled addition
8
3
0
1
3/4: 0 1 1 1
2/4: 0 1 0 1
1/4: 0 0 0 1
2/4: 1 0 0 1
Clip(3/4+2/4+1/4+2/4)=1
1 1 1 1
+

## Slide 45
uNSADD: unipolar
uGEMM – Non-scaled addition
Cycle | Input count (PC) | Acc (1) | Acc (3) | Acc (1>3) | Output
1 | 4 | 4 | 0 | True | 1
2 | 1 | 5 | 1 | True | 1
3 | 2 | 7 | 2 | True | 1
4 | 1 | 8 | 3 | True | 1
4/4
Clip(3/4+2/4+1/4+2/4)=1
3/4: 0 1 1 1
2/4: 0 1 0 1
1/4: 0 0 0 1
2/4: 1 0 0 1
1 1 1 1

## Slide 46
uNSADD
  Expected function
  Output tracking mechanism
    Difference between anticipated and historical output 1s indicates what to output.
uGEMM – Non-scaled addition
Anticipated
Historical

## Slide 47
Input insensitivity
  Multiplication
    Generating operand conditionally
    Ignoring correlation
uGEMM – Processing element

## Slide 48
Input insensitivity
  Multiplication
    Generating operand conditionally
    Ignoring correlation
  Addition
    Caring about bit count
    Ignoring bit distribution
uGEMM – Processing element

## Slide 49
uGEMM – PE array
High parallelism via broadcasting
Input insensitivity due to PE
Reliable early termination
  Fully streaming computation
  High accuracy and stability
Notes: I didn't completely get what you mean by "fully streaming"?

## Slide 50
Outline
Background
Motivation
Architecture
Evaluation

## Slide 51
uMUL performance: Unipolar
Accurate final result
  Static input (ST)
  In-stream input (IS)
Faster stabilization
  Output/Input stability
Input insensitivity
  Rate coding (RC)
  Temporal coding (TC)
Notes: The font on figures is small. Maybe just regenerate a graph with bigger font just for ppt.

## Slide 52
ADD performance: uSADD and uNSADD
Accurate final result
Faster stabilization
Input insensitivity
First to support bipolar non-scaled addition

## Slide 53
uGEMM performance
Accurate final result
  Cross out all configurations
Computing cycle
Notes: If you want to go through comparative results, each column comes in one slide (example comparative study for unipolar scaled is in one slide) with one line for takeaway from results. So many graphs on one slide may confuse viewers.

## Slide 54
uGEMM performance
Accurate final result
  Cross out all configurations
Computing cycle
Notes: If you want to go through comparative results, each column comes in one slide (example comparative study for unipolar scaled is in one slide) with one line for takeaway from results. So many graphs on one slide may confuse viewers.

## Slide 55
uGEMM performance
Accurate final result
  Cross out all configurations
Reliable early termination
  Earlier stable point
Computing cycle
Notes: If you want to go through comparative results, each column comes in one slide (example comparative study for unipolar scaled is in one slide) with one line for takeaway from results. So many graphs on one slide may confuse viewers.

## Slide 56
uGEMM performance
Accurate final result
  Cross out all configurations
Reliable early termination
  Earlier stable point
Computing cycle
Notes: If you want to go through comparative results, each column comes in one slide (example comparative study for unipolar scaled is in one slide) with one line for takeaway from results. So many graphs on one slide may confuse viewers.

## Slide 57
uGEMM performance
Accurate final result
  Cross out all configurations
Reliable early termination
  Earlier stable point
Input insensitivity
  Minimal RC/TC difference
Computing cycle
Notes: If you want to go through comparative results, each column comes in one slide (example comparative study for unipolar scaled is in one slide) with one line for takeaway from results. So many graphs on one slide may confuse viewers.

## Slide 58
uGEMM performance
Accurate final result
  Cross out all configurations
Reliable early termination
  Earlier stable point
Input insensitivity
  Minimal RC/TC difference
Computing cycle
Notes: If you want to go through comparative results, each column comes in one slide (example comparative study for unipolar scaled is in one slide) with one line for takeaway from results. So many graphs on one slide may confuse viewers.

## Slide 59
MLP performance
Final accuracy
  FP-32bit : 96.87%
  FXP-8bit: 96.08%
  uGEMM: 94.7%
  Gaines: 88.58%
Cycle count for 95% final accuracy
  uGEMM: 71
  Gaines: 195

## Slide 60
uGEMM Energy efficiency
Compared to other unary designs
  Higher energy efficiency, though slightly higher area
Compared to binary bit-parallel designs
  Comparable for matrix multiplication
  10X higher for matrix convolution
Compared to binary bit-serial designs
  5X higher for matrix convolution
Notes: Remove all equations
Add animations
Compare with gaines design for uMUL unipolar (add), and uSADD (mux)
You may get questions as to why higher energy costs for each case.

## Slide 61
Thank you!
Q & A